## Slide 1
Widefield + Ephys Analysis Pipeline
Overview of steps 1-9
Step 1
Extract NEV stim
+ camera timing
Step 2
Align widefield
with NEV
Step 3
Build day
pointer/container
Step 4
Pixelwise fluorescence
drift analysis
Pre-step B
Draw brain mask
(brain_mask.mat)
Step 5 (optional - whole-brain analysis)
Compute whole-brain pixelwise dF/F(x,y,t)
5_A - Method 0
Per-trial baseline
dF/F = (F-F_pre_trial)/F_pre_trial
5_B1 -> 5_B2 - Method 1
Global baseline (F_global)
dF/F = (F-F_global)/F_global
Steps 6-7-8 (optional - V1 analysis)
Retinotopy, relink, V1-restricted dF/F
Step 6
Retino align,
define V1 mask
Step 7
Relink day pointer
to V1 day_setup
8_A - Method 0
Per-trial baseline
(V1-restricted)
8_B1 -> 8_B2 - Method 1
Global baseline
(V1-restricted)
Step 4 (V1 version)
Re-run after steps 6+7
Step 9 (required)
Per-pixel significance thresholding
9_A - Method 0
Threshold from movie's
own pre-stim std
9_B - Method 1
Threshold from global
std_dff_m1 (5_B1/8_B1)

## Slide 2
Step 4: Pixelwise Fluorescence Drift Analysis
baseline_drift_analysis_4.m
• Goal: check whether raw fluorescence F(x,y) is stable across the session, before choosing a dF/F baseline method in step 5/8.
• Uses every 0 uA (no-stimulation) trial, all channels pooled.
• For each trial, the full TIFF stack is reduced to a single mean image (one H×W data point per trial), then discarded.
• Per pixel, fits a linear model: F(x,y) = slope · t_onset + intercept, where t_onset is the trial's onset time in session-clock seconds.
• Computes R² in closed form from accumulated sums (single pass, no second loop).
Outputs
• baseline_drift_4.mat
(slope_map, intercept_map, r2_map)
• baseline_drift_slope_r2.png
• baseline_drift_summary_scatter.png
Run twice
Whole-brain version: right after step 3,
using the brain mask.
V1 version: after steps 6+7, restricted
to V1 pixels (V1-aware day_setup).
Interpretation: a flat slope map and trendless scatter -> baseline is stable (Method 0, per-trial baseline, is fine).
Significant drift -> prefer Method 1 (F_global from steps 5_B1/8_B1), which pools ~12,000 frames across the whole session.

## Slide 3
Step 5: Whole-Brain Pixelwise dF/F(x,y,t)
Two baseline normalization methods - same output format, both feed step 9
Method 0 (Step 5_A)
Per-trial baseline
Definition
dF/F(x,y,t) = [F(x,y,t) - F_pre_trial(x,y)] / F_pre_trial(x,y)
F_pre_trial = mean F over THIS trial's pre-stim frames
• Each trial normalized by its own ~10-frame pre-stim window.
• Standard approach; does not require step 4's output.
• Saves per-trial movies dff_ch{N}_{I}uA_trial{K} and a trial-averaged mean_dff_movie.
• Best when raw F is stable within each trial but may drift slowly across the session.
Method 1 (Steps 5_B1 -> 5_B2)
Global baseline
Definition
Step 5_B1: F_global(x,y) = mean F over ALL frames
of ALL 0 uA trials (one-pass accumulation)
std_dff_m1(x,y) = std[(F-F_global)/F_global] (used in step 9_B)
Step 5_B2: dF/F(x,y,t) = [F(x,y,t) - F_global(x,y)] / F_global(x,y)
• Single session-wide baseline (~12,000 frames per pixel) instead of ~10.
• Same baseline used for the dF/F signal AND the step 9_B noise threshold -> self-consistent.
• Saves global_baseline_m1.mat, then per-trial/mean dF/F movies under method1/ch{N}_{I}uA/.
• Best when raw F drifts across the session (see step 4).

## Slide 4
Step 9: Per-Pixel Significance Thresholding
Required for all paths - applies a |dF/F| > n_std · threshold mask to a dF/F movie
Method 0 (Step 9_A)
Within-trial pre-stim std
Threshold definition
pixel_std(x,y) = std( dF/F(x,y, t<0) )
sig_threshold(x,y) = n_std × pixel_std(x,y)
• Threshold computed from THIS movie's own pre-stim frames (~10 samples per pixel).
• Works on any dF/F movie from step 5_A or 8_A.
• Default n_std = 3 (~0.3% of Gaussian baseline samples cross by chance).
• Output tagged e.g. thresh_mean_dff_ch16_7uA_3σ.mat
Method 1 (Step 9_B)
Global std threshold
Threshold definition
std_dff_m1(x,y) <- loaded from
global_baseline_m1.mat (5_B1) or
global_baseline_m1_v1.mat (8_B1)
sig_threshold(x,y) = n_std × std_dff_m1(x,y)
• Threshold derived from ~12,000 frames of 0 uA null data per pixel, far more robust than ~10.
• Works on dF/F movies from step 5_B2 or 8_B2 (Method 1 dF/F).
• Same |dF/F| > sig_threshold logic and frame-grid/video output as Method 0.
• Output tagged e.g. thresh_mean_dff_m1_ch16_7uA_0.3σ_m1.mat

## Slide 5
Step 5_B — Drift-Corrected dF/F (Method 1)
Step 4 linear model gives each trial its own time-varying baseline · F_baseline(x,y) = intercept(x,y) + slope(x,y) · t_session
Session time →
Raw F ↑
old: constant F_global
new: F_baseline(t) = intercept + slope · t
F_b(t₁)
Trial 1 (early)
over-corrects
F_b(t_k)
Trial k (mid)
F_b(t_N)
Trial N (late)
under-corrects
Using constant F_global: baseline is wrong for early AND late trials — a systematic bias in dF/F
Using drift-corrected F_baseline(t): each trial's normalisation tracks the actual fluorescence level at that moment
Step 4 output (baseline_drift_4.mat)
slope_map(x,y) [ΔF / second]
intercept_map(x,y) [F at t = 0 s]
For each trial (onset frame → session clock time)
t_session = (onset_frame − 1) / Fs
F_baseline(x,y) = intercept_map + slope_map × t_session
dF/F(x,y,t) =
[ F(x,y,t) − F_baseline(x,y) ] / F_baseline(x,y)
Each trial is normalised by the expected fluorescence at its own
point in session time — drift is removed before computing dF/F.